## Slide 1: PVT introduction
Khalil Kashefi
7 May 2021

## Slide 2: Outline
  Phase diagram
  Equation of states
  Flash calculation

## Slide 3: Phase Diagrams
  A picture is worth a thousand words!
Pure-component systems
Mixtures
graphical method
large amount of information
more components, more the complexity
P-T P-V

## Slide 4: Phase Diagrams – Pure component
  Water!
    Tb --> Pb
    dew point curve and the bubble point curve
P
T
Liquid
Vapour
Dew Point: The pressure and temperature condition at which a droplet exists in equilibrium with a vapor system.
Bubble Point: The pressure and temperature condition at which the system is all liquid, and in equilibrium with a bubble of gas.
behavior at different conditions?
100 C
1 bar

## Slide 5: Phase Diagrams – Pure component
  Critical point
P
T
Liquid
Vapour
Temperature and pressure for which liquid and vapor are no longer distinguishable.
Pc
Tc
Critical Point
Supercritical region
Gasous phase
liquid and gas are in equilibrium along the vapor pressure curve.

## Slide 6: Phase Diagrams – Pure component
  Isobaric heating
  A path without phase change
    liquid, or high-density (A) to a gas, or low-density (B)
  Supercritical fluid (SCF)
  CO2
    31 °C, 73.8 bar
    expanding to fill its container like a gas but with a density like that of a liquid!
    SC-CO2 may act differently!! when neighboring hydrocarbon
P
T
Liquid
Vapour
A
D
B
E
F
C
SCF

## Slide 7: Phase Diagrams – Pure component
  PV diagram
T = constant
Dew Curve
Bubble Curve

## Slide 8: Phase Diagrams – mixture
P
T
Liquid
Vapour
C
P
T
V+L
C
Liquid
Vapour
mixture
Res - Oil
Res - Gas
Production / transport line
Fluid | Composition
Dry gas | C1
Wet gas | C1-C6
Gas condensate | C1-C8
Volatile oil | C1-C12
Black oil | C1-C20+
Heavey oil | > C20+

## Slide 9: Phase Diagrams ?
P
T
V+L
C
Lsingle
Vsingle
L1 + V
L1 + L2 + V
L1 + L2
oil phase (L1)
CO2 rich vapor phase (V)
CO2 rich Liquid phase (L2)
Hydrocarbon/CO2
high content
Is this wrong, and it is just not converged?
Do we have such a this fluid system?
subsea CO2
?

## Slide 10
oil phase (L1)
CO2 rich vapor phase (V)
CO2 rich liquid phase (L2)
V/L2 interface
L1/L2 interface

## Slide 11: Equations of State
  The principal thermodynamic models are the equations of state (EoS).
  Phase behavior data: Laboratory measurements, expensive; Field data, you would lose valuable resources or have to stop operations to make your observations.
  Why do we need an Equation of State? To define the state of the system and to determine the properties of the system at that state.
  Given a fluid, with EOS, possible to predict its behavior at any condition of pressure, temperature and volume (P-V-T).
  In other words, we want to describe the P-V-T behavior of fluids in general.

## Slide 12: Equations of State - ideal
Negligible interactions between the molecules,
Its molecules occupy no volume (negligible molecular volume),
Collisions between molecules are perfectly elastic — this is, no energy is lost after colliding.
ideal behavior may be approached by real gases at low P and high T, where the distance between any pair of gas molecules is great.

## Slide 13: Equations of State - ideal
T = T1
Dew point
Bubble point
Real behaviour

## Slide 14: Equations of State – Cubic Behavior
Dimensionless point!
Particles do not interact when they collide (elastic collision)
HP - LT
a
b
Depends on the strength of the attraction
Correction for the volume occupies by the molecule itself

## Slide 15: Equations of State – Cubic Behavior
T1 = constant
isotherm
P1
P3
P2

## Slide 16: Equations of State – Cubic EOS
mixing rules
CO2 / hydrocarbon

## Slide 17: Advantages of cubic EoS
They are simple models capable of fast calculations.
They are applicable over a wide range of pressures and temperatures.
They are capable of describing properties of compounds in both liquid and vapor phases, and can therefore be used to predict phase equilibrium properties, such as vapor pressure.
There is no need, in most cases, for more than one interaction parameter for gas–hydrocarbons and good correlations for such mixtures are obtained.
Satisfactory results are obtained both for low- and high-pressure VLE.
Often good multicomponent VLE prediction is achieved for mixtures containing hydrocarbons, gases and other non-polar compounds (using interaction parameters from binary data).
Many existing databases and correlations are available for kij.

## Slide 18: Shortcoming of cubic EoS
Calculations may, in some cases, be sensitive to the interaction parameter, kij, especially for gas– hydrocarbons.
Interaction parameters, often kij, depend on temperature.
Cubic EoS do not yield liquid volumes in good agreement with experimental values, unless a volume translation is used.
Results are poor for complex, multicomponent VLE and LLE, especially in the presence of associating compounds and water.
LLE of highly immiscible systems is not correlated satisfactorily. In most cases, a single interaction parameter cannot represent both solubilities in such systems. In general, LLE is not very well correlated with cubic EoS even for non-polar systems, e.g. CO2–decane at low temperatures.
Notes: They are called association models. The association models are particularly suitable for describing phase equilibria of mixtures containing highly polar and/or strongly associating compounds such as water, alcohols, acids, amines, phenols and others which have the capability of forming hydrogen bonds. The hydrogen bonding formation between molecules of the same kind is called self-association (e.g. in pure water or pure methanol), while the creation of hydrogen bonding complexes between two different molecules is called cross-association (e.g. water–methanol)

## Slide 19: Advanced EOS
Statistical Associating Fluid Theory (SAFT)
  perturbed-chain SAFT (PC-SAFT)
  .....
Cubic-Plus-Association EoS (CPA)
SAFT parameters
SRK
(can be any cubic-EOS)
association term
similar to SAFT
CPA parameters

## Slide 20: Some tips and concepts…
Vapour
Liquid
Thermodynamic equilibruim
Net Q = 0
But we have
heat transfer!!
F
P, T

## Slide 21: Some tips and concepts…
Vapour
Liquid
Saturation Pressure & Temperature
Vapor pressure
Partial pressure
P
T
Liquid
Vapour
P & T
Vapour pressure @ T
A, B, C
P total = PA + PB + PC
PA = yA × P total
PA = xA × P*A
A, B, C

## Slide 22: Some tips and concepts…
Chemical potential (μ)
Fugacity (f)
Fugacity coefficient (Φ)
Equilibrium
chemical potential (μ) of a species is energy that can be absorbed or released due to a change
V
L
A, B,...
A, B,...
μVA=μLA
μVB=μLB
μi
fi
pi
μ
P
real
ideal
Fugacity: Tendency to escape
Thermodynamic equations....
fVA = fLA
fVB = fLB
Φi = fi /pi

## Slide 23: Flash Calculation
Typical problem to solve:
Given:
T, P , F, and Zi
Find:
V, yi, L, xi
F
Zi
V
yi
L
xi
i = 1, 2, 3,...
P
T

## Slide 24: Flash Calculation
F = L + V
F . zi = L . xi + V . yi
yi = Ki . xi
∑ yi = 1
∑ xi = 1
V
yi
L
xi
F
Zi
P
T
xi = zi / [1 + (Ki – 1)(V/F)]
yi = Ki . Zi / [1 + (Ki – 1)(V/F)]
VLE

## Slide 25: Flash Calculation
xi = zi / [1 + (Ki – 1)(V/F)]
yi = Ki . Zi / [1 + (Ki – 1)(V/F)]
∑ yi = 1
∑ xi = 1
Rachford Rice equation
(1) Ki = P*i / P t
(3) xi and yi
(2) V/F
Dalton and Raoults laws
Ideal gas & solution
Different methods to calculate...

## Slide 26: K-values
Function of T, P and zi
Experimental
K-value charts
-light hydrocarbon
-limitted pressure
-numerous curve fitted available
for calculation of K-values.
- Wilson eq. is an example:

## Slide 27: K-values
Experimental
K-value charts
Raoult’s Law
vapor phase behaves as an ideal gas and the liquid phase is an ideal solution.

## Slide 28: K-values
Experimental
K-value charts
Raoult’s Law
EoS Approach
V
L

## Slide 29: Fugacity Coefficient
Flash Calc.
Pure component
Mixture
Equations of State – EoS

## Slide 30: Flash Calculation
Rachford Rice equation
Ki = f (P, T, xi, yi)
xi, yi, L, V
V/F
Ki = f (T, P, xi, yi)
appropriate iterative scheme…

## Slide 31: Flash Calculation Successive Substitution Method (SSM)
xi = zi / [1 + (Ki – 1)(V/F)]
yi = Ki . Zi / [1 + (Ki – 1)(V/F)]
Known: T, P , F, and Zi
Guess Ki
ex. Wilson eq.
V
Ki
xi, yi
Using EoS
calculate fugacity (fG)
fG =? fL
fG, fL
Using EoS
calculate fugacity (fL)

## Slide 32
Next step:
Knowing the behavior of the CO2/hydrocarbon system is important for us.
I would suggest to gather the PVT data on this system available in the literature, with the aim of:
Analysing the behaviour of CO2/hydrocarbon system at different conditions and different fluids.
The PVT data would help us in validating the models and codes in our project.
Any other suggestions?